## Slide 1: GridPACK™: Framework and Library for Accelerating HPC in Grid Applications
Bruce Palmer, William Perkins, Yousu Chen, Renke Huang, Zhenyu (Henry) Huang
IEEE PES hpcGrid WG Webinar
July 16, 2018

## Slide 2: Acknowledgement
Webinar Sponsor:
  IEEE Power and Energy Society Working Group on High Performance computing for Grid Applications (hpcGrid WG)
Funding Sponsors:
  US Department of Energy (DOE) Office of Electricity (OE) Advanced Grid Modeling (AGM) Program
  US Department of Energy (DOE) Grid Modernization Laboratory Consortium (GMLC)
  US Department of Energy (DOE) Office of Advanced computing Scientific Research (ASCR)
  US Department of Energy (DOE) Advanced Research Program Agency – Energy (ARPA-E)
  Bonneville Power Administration (BPA) Technology Innovation Program

## Slide 3: Math and computing challenges in modeling and simulation of the future grid
103 104 105 106 108 109
Generation Transmission Substation Transformer Site Load
Multi-scale spatio-temporal modeling and simulation with stochasticity
  From micro-second to decades
  From 103 generators nodes to 109 end-use devices
Large-scale data assimilation for state and parameter calibration
  Petabyte data/year from high-speed sensors and smart meters.
Modeling of multi-system dynamics and dependency
  Grid, buildings, communication, gas pipelines, weather/wind/solar, water
15 years 10 years 5 years 1 year 1 month 1 week 1 day 5 minutes μ-seconds
Spatial Temporal
Notes: Interaction among systems. Multiscale problem

## Slide 4: Why use High Performance Computing (HPC) for the Power Grid?
The power grid is growing more complex
  More renewables
  Smart grid technology
Serial codes are no longer enough
  Simulation of larger and more complex models
  Reduced time to solution for operations
  Evaluation of thousands (N-1) or millions (N-2) of contingencies
  Large scale optimization

## Slide 5: Does Parallel Computing Help?
Time to Solution
Number of Processors
Computation Bound
Communication Bound
Big Problem
Small Problem

## Slide 6: Power Grid Computing Challenges
Faster time to solution for operations
Large number of scenarios to account for uncertainties and increasing variability
More complicated algorithms and more detailed models
Optimization problems are increasing in size and complexity
Significant gap in program complexity in going from serial to parallel code

## Slide 7: Example Success: Fast State Estimation captures the changes and offers an opportunity to stop cascading
For the first time, the core function in control rooms – State Estimation – can run at a unprecedented 0.5s speed (>40x faster).
Chart: September 8, 2011 Pacific Southwest Blackout
 | 10 | 27 | 234 | 3 | 2 | 205 | 60 | 0.1 | 0.1 | 61 | 14 | 0.1 | 3 | 4 | 19 | 0.1 | 17
Traditional view, >20 sec
Need for speed
improvement
When the event interval is less than the ability to respond, there is a cascading effect. This means that the region of impact from the disturbance is expanding.
SCADA interval, ~5 sec
New, 0.5 sec view

## Slide 8: Example Success: Visual analytics of massive contingency analyses for real-time decision support
Current tabular format presents data, not information
New visualization tool converts data to actionable info
Easy-to-interpret visualization with prioritized concerns & recommendations
Operators reported 30% improvement in emergency response
Contingency | # of scenarios | Serial on 1 core | Parallel on 512 cores | Parallel on 10,240 cores
WECC N-1 (full) | 20,000 | 39 minutes | 4.8 seconds | 
WECC N-2 (partial) | 1,000,000 | 68.5 hours | 8 minutes (511x speedup) | 25 seconds (9871x speedup)
ERCOT | 1,000,000 | ~4 hours (estimated) | ~0.5 minute (estimated) | <2 seconds (estimated)
Eastern Interconnect | 1,000,000 | ~1100 hours (estimated) | ~128 minutes (estimated) | ~400 seconds (estimated)

## Slide 9: Example Success: Real-time path rating through fast computation to manage transmission congestion
Look-Ahead Dynamic Simulation
  16,000-bus w/ simplification
  9 sec for 30-sec simulation
  13X faster than today’s commercial tools
Real-Time Path Rating in 10 min
  Significant congestion cost: NYISO $1.1B/2010; PJM $1.4B/2012
  Transmission expansion?
  Realistic ratings: +1000 MW = +$240M/year
  Avoid renewable curtailment
Chart: Number of threads
Total | 1 | 1.9193 | 3.6295 | 6.6996 | 15.2523 | 22.0038 | 25.6792
1 2 4 8 16 32 64
26X
tap into unused capacities

## Slide 10: GridPACK Approach
Lower the threshold for development of HPC codes
Create high level abstractions for common programming motifs
Encapsulate high performance math libraries
Compartmentalize functionality and promote reuse of software components
Hide communication and indexing

## Slide 11: GridPACK Framework
GridPACK is written in C++ and is highly customizable
  Inheritance
  Software templates
Runs on Linux-based clusters and workstations.
Wide variety of solvers and parallel linear algebra available through PETSc suite of software.
Prebuilt modules
  Power flow
  State estimation
  Dynamic simulation
  Dynamic state estimation (Kalman filter)
Robust support for task-based execution.

## Slide 12: GridPACK Core Framework
Core Data Objects
Power Grid Network
Matrices and Vectors
Application Driver
Base Network Components
Neighbor Lists
Matrix Elements
Math and Solver Module
PETSc
Mapper
Network Module
Exchanges
Partitioning
Task Manager
Import Module
PTI Formats
Dictionary
Export Module
Serial IO
GridPACK™ Framework
Configure Module
XML
GridPACK™ Applications
Utilities
Errors
Profiling
Base Factory
Network-wide Operations
Application Factory
Application Components

## Slide 13: Major GridPACK Modules
Network: manages the topology, neighbor lists, parallel distribution and indexing
Components: define the behavior and properties of bus and branch
Mapper: Creates distributed matrices and vectors from network components
Factory: manages interactions between network and the components
Math: generic wrapper on top of parallel math libraries
Components
Network
Mappers
Math
Factory

## Slide 14: GridPACK Functionality
What you supply
  Bus and branch classes that define your power system application
  High level application driver describing solution procedure
What you get
  Parallel network distribution and setup
  Data exchanges between processors
  Parallel matrix builds and projections
  I/O of distributed data
  Parallel solvers and linear algebra operations
  Distributed task management
  Application modules for use in more complex workflows

## Slide 15: GridPACK Application
GridPACK
Bus Class
Branch Class
Algebraic Equations
Algorithms
Matrix Operations and Solvers
PETSc HPC Math Library
MPI
Global Arrays
ParMetis
Power Grid Application

## Slide 16: Software Reuse
GridPACK Component or Module
User Component or Module
User Component or Module
Inherit from GridPACK component or module to create a new application
Rename and modify existing GridPACK component or module to create a new application
Use GridPACK components and/or modules as is

## Slide 17: Distributed Power Flow Jacobian from Mapper
16351 bus WECC system

## Slide 18: Power Flow Code
1 typdef BaseNetwork<PFBus,PFBranch> PFNetwork;
2 Communicator world;
3 shared_ptr<PFNetwork>
4 network(new PFNetwork(world));
5
6 PTI23_parser<PFNetwork> parser(network);
7 parser.parse("network.raw");
8 network->partition();
9 typedef BaseFactory<PFNetwork> PFFactory;
10 PFFactory factory(network);
11 factory.load();
12 factory.setComponents();
13 factory.setExchange();
14
15 network->initBusUpdate();
16 factory.setYBus();
17
18 factory.setSBus();
19 factory.setMode(RHS);
20 BusVectorMap<PFNetwork> vMap(network);
21 shared_ptr<Vector> PQ = vMap.mapToVector();
22 factory.setMode(Jacobian);
23 FullMatrixMap<PFNetwork> jMap(network);
24 shared_ptr<Matrix> J = jMap.mapToMatrix();
25 shared_ptr<Vector> X(PQ->clone());
26
27 double tolerance = 1.0e-6;
28 int max_iteration = 100;
29 ComplexType tol = 2.0*tolerance;
30 LinearSolver solver(*J);
31
32 int iter = 0;
33
34 // Solve matrix equation J*X = PQ
35 solver.solve(*PQ, *X);
36 tol = X->normInfinity();
37
38 while (real(tol) > tolerance &&
39 iter < max_iteration) {
40 factory.setMode(RHS);
41 vMap.mapToBus(X);
42 network->updateBuses();
43 vMap.mapToVector(PQ);
44 factory.setMode(Jacobian);
45 jMap.mapToMatrix(J);
46 solver.solve(*PQ, *X);
47 tol = X->normInfinity();
48 iter++;
49 }

## Slide 19: GridPACK Task Manager Support
World Group
Parallel tasks running on subgroups

## Slide 20: Multiple Levels of Parallelism
8 tasks, 4 processors
8 processors
16 processors (2 levels of parallelism)

## Slide 21: Dynamic Contingency Analysis
Simulation of 16 contingencies on 16351 bus WECC network
Two-level parallelism starts here

## Slide 22: GridPACK Examples

## Slide 23: Dynamic Simulation Mini-Framework
Dynamic Simulation Application
DS Bus Component
DS Branch Component
Base Generator
Base Exciter
Base Governor
:
Base Generator
Base Exciter
Base Governor
Base Relay
Base Relay
Base Relay
:
Base Relay
Base Relay
Base Relay
:
GENCLS
GENROU
GENSAL
EXDC1
WSIEG1
ESST1A
ESST4B
WSHYGP
GGOV1
LVSHBL
FRQTPAT
DISTR1
:

## Slide 24: Dynamic simulation of WECC system
WECC system of 17,000 buses with detailed dynamic models, 20 seconds simulation, results compared with PowerWorld.
Achieve Faster-than-real-time simulation with 16 cores.
No. of Cores | Total Solution Time (seconds)
1 | 72.92
2 | 45.04
4 | 30.96
8 | 22.95
16 | 19.57

## Slide 25: Module-Based Simulations
Contingency Analysis
Real-Time Path Rating
Dynamic Security Assessment under Uncertainty
GridPACK™ Framework
Y-Matrix Components
PF-Matrix
DS-Matrix
SE-Matrix
PF-Module
DS-Module
SE-Module
User Applications

## Slide 26: Many Task Simulations
Task Manager
Time
Processors
Program Setup and Task Initialization
T1
T2
T3
T4
T5
T6
T7
T8
T9
T10
T11
T11
Result Collection and Second Stage Task Initialization
T1
T2
T3
T4
T5
T6
T7
T8
T9
T10
T11
T12
T13
T14
T15
Task Manager

## Slide 27: Application (1): Contingency Analysis
Static Contingency Analysis of WECC system using 1 processor per contingency for 3638 contingencies
Contingency Analysis
GridPACK™ Framework
PF-Matrix
PF-Module
Y-Matrix Components
Task Manager

## Slide 28: Example (2): Dynamic Contingency Analysis
Simulation of 16 contingencies on 16351 bus WECC network
2 levels of parallelism
Dynamic Contingency Analysis
GridPACK™ Framework
PF-Matrix
PF-Module
Y-Matrix Components
Task Manager
DS-Matrix
DS-Module

## Slide 29: Application (3): Dynamic Security Assessment (DSA) under Uncertainty
Dynamic Security Assessment under Uncertainty
GridPACK™ Framework
Y-Matrix Components
PF-Matrix
DS-Matrix
SE-Matrix
PF-Module
DS-Module
SE-Module
User Applications
Updated bus components based on realizations that covers forecast errors

## Slide 30: Application (3) DSA under Uncertainty
The quantiles of all the contingencies for each generator are used to represent the statistical characteristics at each time stamp.
The lower/upper bounds use 1.5 interquartile range (IQR).
Line flow under different contingencies with different quantiles and IQR
Rotor speed under different contingencies with different quantiles and IQR

## Slide 31: GridPACK Summary
Open source software for running HPC power grid simulations
Written in C++ and designed to run on Linux platforms with MPI
Many applications already available
  Power flow
  Dynamic simulation
  State estimation
  Kalman Filters
Can be reused to develop own applications
Download and documentation at www.gridpack.org
Contact us at gridpack.account@pnnl.gov

## Slide 32: Accessing GridPACK
Download from www.gridpack.org
Extensive documentation in GridPACK user manual
Documentation on building GridPACK on numerous different platforms. If you run into problems, we can help
Contact us at gridpack.account@pnnl.gov

## Slide 33: Extra Slides

## Slide 34: Customizing Networks using the BaseNetwork Class
Template class that can be created with arbitrary user-defined types for the buses and branches
  BaseNetwork<MyBus, MyBranch>(const Communicator &comm)
Implements partitioning of network between processors
  Create highly connected sub-networks on each processor with minimal connections between processors
Implements data exchanges between buses and branches on different processors
Manages indexing of network components

## Slide 35: Customization Through Templates
GridPACK Framework
User Code
Buses
Branches

## Slide 36: Network Topology
Bus
Branch

## Slide 37: Partitioning the Network
Process 0
Process 1

## Slide 38: Partitioning of Network
WECC (Western Electricity Coordinating Council) network partitioned between 16 processors

## Slide 39: Multiple Networks
Process 0
Process 1

## Slide 40: Multiple Distributed Networks
Process 0
Process 1
Process 2
Process 3

## Slide 41: Component Classes
Each bus and branch in the network has an associated bus or branch object. They also have an associated DataCollection object
The bus and branch classes are written by the user. Access to other functionality in GridPACK is through functions defined in the bus and branch interfaces
  Creation of matrices and vectors
  IO
  Data exchange between processors
  Creation of optimization equations

## Slide 42: Traditional Programming to Evaluate Yii
integer nbus
integer attached_branch_start(nbus+1)
integer attached_branch_nghbrs(n_neighbors)
for ibus = 1, nbus
ibeg = attached_branch_start(ibus)
iend = attached_branch_start(ibus+1)-1
ydiag(ibus) = 0.0
for j = ibeg, iend
ibranch = attached_branch_nghbrs(j)
x = reactance(ibranch)
r = resistance(ibranch)
c = cmplx(r,x)
ydiag(ibus) = ydiag(ibus)+1.0/c
end do
end do
Properties are in large lists with auxiliary data structures maintaining relationships between different pieces of data

## Slide 43: C++ Programming to Evaluate Yii
int nbus = network->numBuses()
for (int ibus=0; ibus<nbus; ibus++) {
Bus *bus = network->getBus(i);
std::vector<Branch> branches = bus->getNeighborBranches();
DoubleComplex y(0.0,0.0);
for (j=0; j<branches.size(); j++) {
Branch *branch = branches[j];
double r = branch->getResistance();
double x = branch->getReactance();
DoubleComplex c(r,x);
y += 1.0/c;
}
bus->setYdiag(y);
}
Data is tied to individual objects instead of being associated with large. global lists

## Slide 44: Component Class Hierarchy
MatVecInterface
BaseComponent
BaseBusComponent
BaseBranchComponent
AppBusComponent
AppBranchComponent
GenMatVecInterface

## Slide 45: Component Reuse
BaseBusComponent
BaseBranchComponent
Y-Matrix Bus Component
Y-Matrix Branch Component
Powerflow Bus Component
Powerflow Branch Component

## Slide 46: Mapper
Provides a flexible framework for constructing matrices and vectors representing power grid equations
Hide the index transformations and partitioning required to create distributed matrices and vectors from application developers
Developers can focus on the contributions to matrices and vectors coming from individual network elements

## Slide 47: Mapper
1
2
3
4
5
6
7
8
12
11
10
9

## Slide 48: Matrix Contributions from Components
1
2
3
4
5
6
7
8
12
11
10
9
No matrix contribution
No matrix contribution
No matrix contribution

## Slide 49: MatVecInterface
// Implemented on buses
virtual bool matrixDiagSize(int *isize,
int *jsize) const
virtual bool matrixDiagValues(ComplexType *values)
// Implemented on branches
virtual bool matrixForwardSize(int *isize,
int *jsize) const
virtual bool matrixReverseSize(int *isize,
int *jsize) const
virtual bool matrixForwardValues(ComplexType *values)
virtual bool matrixReverseValues(ComplexType *values)

## Slide 50: Distribute Component Contributions and Eliminate Gaps